## Slide 1
MOOSE Stochastic Tools Module Training Session
Developers: Som Dhulipala, Zach Prince, Peter German
MOOSE International Workshop 2025
03/13/2025

## Slide 2: The MOOSE Stochastic Tools Module
Provide a MOOSE interface for performing stochastic analysis on MOOSE-based models.
Sample parameters, run applications, and gather data that is both efficient (memory and runtime) and scalable.
Perform UQ and sensitivity analysis with distributed data with advanced variance reduction methods
Parallel Scalable Inverse Bayesian UQ for parameter and model error estimation
Train meta-models to develop fast-evaluating surrogates of the high-fidelity multiphysics model
  Harness advanced machine learning capabilities through the C++ front end of Pytorch [1]
  Use active learning models for building surrogates
Provide a pluggable interface for these surrogates.
Use POD (Proper Orthogonal Decomposition)-based dimensionality reduction methods to build mappings between solution variables and latent (low-dimensional) spaces
POD modes of a 2D heat conduction problem
UQ on modeling TRSIO Particle Ag release
General process for forward UQ
Introduction

## Slide 3: Recent developments in MOOSE STM
Parallel Markov chain Monte Carlo: for Bayesian UQ
Gaussian process variants
Parallel active learning

## Slide 4: Focus of this training session
Introduction
Part 1: forward uncertainty quantification
  Uncertainty propagation through Monte Carlo sampling
  Sensitivity analysis using Sobol indices
  Rare events analysis using parallel subset simulation [EXCLUDE]
Part 2: Bayesian (inverse) uncertainty quantification
  Model parameter uncertainties
  Model parameter + noise uncertainties
  Model parameter + noise + model inadequacy uncertainties
Part 3: active learning
  Training a Gaussian process surrogate with Monte Carlo sampling
  Use of an acquisition function
  Solving optimization problems with Bayesian optimization
TRISO fuel fission product release

## Slide 5: Part 1: Forward uncertainty quantification
  Uncertainty propagation through Monte Carlo sampling
  Sensitivity analysis using Sobol indices
  Rare events analysis using parallel subset simulation

## Slide 6: Uncertainty propagation to model outputs
Part 1: Forward UQ
MOOSE computational model
Uncertain input parameters
Uncertain model outputs
Statistics: mean, standard deviation, etc.

## Slide 7: Uncertainty propagation to model outputs
Part 1: Forward UQ
1. Distributions
2. Samplers
3. MultiApps
4. cmdline controls
5. Transfers
6. Reporters

## Slide 8: Sobol sensitivity analysis
Part 1: Forward UQ
MOOSE computational model
Uncertain input parameters
Sensitive input parameters
First order sensitivity indices
Second order sensitivity indices

## Slide 9: Sobol sensitivity analysis
Part 1: Forward UQ
2. Reporters
Sobol reporter
Samplers
Sobol sampler

## Slide 10: Rare events analysis: parallel subset simulation
Part 1: Forward UQ
MOOSE computational model
Uncertain input parameters
Failure probability; input parameter distribution causing model failures
Quantify rare events with failure probabilities ranging 1E-2 to 1E-8

## Slide 11: Rare events analysis: parallel subset simulation
Part 1: Forward UQ
Samplers
Parallel subset simulation sampler
2. Reporters
Adaptive Monte Carlo decision

## Slide 12: Part 2: Bayesian (inverse) uncertainty quantification
  Model parameter uncertainties
  Model parameter + noise uncertainties
  Model parameter + noise + model inadequacy uncertainties

## Slide 13: Quantify model parameter uncertainties
Part 2: Bayesian (inverse) UQ
MOOSE computational model
Unknown input parameters
Probability distributions of best input parameters such that the model predictions match experiments
Experimental data
Model params
Experimental configuration
Experimental value
Model prediction
Required distribution
Likelihood function
Prior

## Slide 14: Quantify model parameter uncertainties
Part 2: Bayesian (inverse) UQ
“Experimental data”
Resultant velocities at 9 locations in the domain
Resultant velocities: experimental data
Locations: experimental configurations
Ux1 = 1.0, Uy1 = 2.5
(treated as unknown)
Predictive model
Predict resultant velocities at 9 locations in the domain
Infer the unknown Ux1, Uy1 such that predictions match experiments

## Slide 15: Quantify model parameter uncertainties
Part 2: Bayesian (inverse) UQ
Distributions
Priors
2. Likelihood
3. Samplers
Differential evolution MCMC

## Slide 16: Quantify model parameter uncertainties
Part 2: Bayesian (inverse) UQ
4. MultiApps and Transfers
5. Controls
6. Reporters
Decision-making

## Slide 17: Computational engine
Part 2: Bayesian (inverse) UQ
Serial Markov chain Monte Carlo (MCMC)
Parallel multiple chain MCMC

## Slide 18: Quantify model parameter + noise uncertainties
Part 2: Bayesian (inverse) UQ
MOOSE computational model
Unknown input parameters
Probability distributions of best input parameters and noise such that the model predictions match experiments
Experimental data
Model params
Noise in the experiments
Experimental configuration
Experimental value
Model prediction
Required distribution
Likelihood function
Prior
Unknown noise

## Slide 19: Quantify model parameter + noise uncertainties
Part 2: Bayesian (inverse) UQ
“Experimental data”
Resultant velocities at 9 locations in the domain
Resultant velocities: experimental data
Locations: experimental configurations
Ux1 = 1.0, Uy1 = 2.5
(treated as unknown)
Added Gaussian noise of 0.4
(treated as unknown)
Predictive model
Predict resultant velocities at 9 locations in the domain
Infer the unknown Ux1, Uy1 such that predictions match experiments
Infer the unknown noise value

## Slide 20: A note on the code architecture
Part 2: Bayesian (inverse) UQ

## Slide 21: Quantify model parameter + noise uncertainties
Part 2: Bayesian (inverse) UQ
Distributions
Priors
2. Samplers
Differential evolution MCMC
(variance) is inferred not (standard deviation)

## Slide 22: Quantify model parameter + noise + model inadequacy uncertainties
Part 2: Bayesian (inverse) UQ
MOOSE computational model
Unknown input parameters
Probability distributions of best input parameters, noise, and model inadequacy such that the model predictions match experiments
Experimental data
Model params
Noise in the experiments + inadequacy in the model
Experimental configuration
Experimental value
Model prediction
Required distribution
Likelihood function
Prior
Unknown noise
Inadequacy in the model

## Slide 23: Quantify model parameter + noise + model inadequacy uncertainties
Part 2: Bayesian (inverse) UQ
“Experimental data”
Resultant velocities at 9 locations in the domain
Resultant velocities: experimental data
Locations: experimental configurations
Ux1 = 1.0, Uy1 = 2.5
(treated as unknown)
Added Gaussian noise of 0.4
(treated as unknown)
Predictive model
Predict resultant velocities at 9 locations in the domain
Infer the unknown Ux1, Uy1 such that predictions match experiments
Infer the unknown noise value

## Slide 24: Part 3: Active learning and Bayesian optimization
  Training a Gaussian process surrogate with Monte Carlo sampling
  Use of an acquisition function (active learning)
  Solving optimization problems with Bayesian optimization

## Slide 25: Training and loading a Gaussian process surrogate
Part 3: Active learning
GP is a Bayesian/probabilistic machine learning model

## Slide 26: Training and loading a Gaussian process surrogate
Part 3: Active learning
Training data
Resultant velocity at the center point in the domain
Ux1, Uy1
(treated as variable inputs)

## Slide 27: Training and loading a Gaussian process surrogate
Part 3: Active learning
1. Distributions
2. Samplers
3. Trainers
4. Covariance
5. Outputs

## Slide 28: Training and loading a Gaussian process surrogate
Part 3: Active learning
Samplers
Test samples
2. Surrogates
Gaussian process
3. Reporters
Evaluate pre-trained GP

## Slide 29: Training a GP with active learning
Part 3: Active learning
- Global surrogate development
- Bayesian UQ
- Rare events analysis
- Optimization
Local penalization

## Slide 30: Training a GP with active learning
Part 3: Active learning

## Slide 31: Training a GP with active learning
Part 3: Active learning
Training data
Resultant velocity at the center point in the domain
Ux1, Uy1
(treated as variable inputs)
Acquisition function: Expected Improvement for Global Fit (EIGF)

## Slide 32: Training a GP with active learning
Part 3: Active learning
1. Sampler
Active learning sampler
3. Trainers
GP active learning trainer
4. Surrogates
Evaluate a GP surrogate
5. Reporters
Active learning decision making
2. ParallelAcquisition

## Slide 33: Bayesian optimization
Part 3: Active learning
Optimization objective
Resultant velocities at 9 locations in the domain
Resultant velocities: experimental data
Do not know Ux1, Uy1
Given experimental data, optimize for Ux1, Uy1
Acquisition functions: Expected Improvement, Probability of Improvement, Upper Confidence Bound

## Slide 34: Bayesian optimization
Part 3: Active learning

## Slide 35: Thank you! (Som.Dhulipala@inl.gov, Peter.German@inl.gov, Zachary.Prince@inl.gov) Acknowledgements: This work is funded by the INL Laboratory Directed Research and Development (LDRD), Nuclear Energy Advanced Modeling and Simulations (NEAMS), Advanced Materials and Manufacturing Technologies (AMMT), and Nuclear Energy University Partnerships (NEUP) programs. This work has utilized the high-performance computing resources at the Idaho National Laboratory.